## Slide 1
SMART INDIA HACKATHON 2026
HARDWARE EDITION | MINISTRY OF EDUCATION & QUALCOMM INC.
PROJECT PHOENIX X
SAR UAV
Dual-Brain Edge-AI Scout for Zero-Infrastructure Disaster Reconnaissance
PROBLEM STATEMENT ID
SIH26177
THEME
Robotics and Drones
PROBLEM STATEMENT TITLE
A deployable AI-powered autonomous drone that aids search-and-rescue operations by detecting people and hazards, thereby improving responder safety and reducing victim discovery time.
SPONSORING ORGANIZATION
CATEGORY
Qualcomm Inc.
Hardware
TEAM NAME
TEAM ID
Phoenix X
141943
WEB DEMO
VIDEO
Qualcomm Dragonwing QRB2210
STM32U5 Zephyr RTOS Flight
Dual RGB + Thermal Fusion
3-5 km LoRa Telemetry
Tait-Bryan Ray-Casting GPS

## Slide 2
Disaster Reconnaissance & Emergency Survivor Triage
2
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
PROBLEM STATEMENT
PROPOSED SOLUTION
INNOVATION / UNIQUENESS
Dual-Brain Architecture
5W Edge YOLO
Ray-Cast Geolocation
ROS-LoRa P2P Bridge
Anti-Compass Drift VIO
TRADITIONAL DISASTER SEARCH
(Current Approach)
Manual Foot Sweeps
Blind Rubble Digging
Stalled at Sunset (Darkness)
High Responder Casualty Risk
Critical Hours Lost
PHOENIX AUTONOMOUS SAR
(Our Approach)
Autonomous Aerial Sweep
24/7 Thermal Night Vision
Instant Survivor GPS Raycasting
Zero-Drop LoRa Telemetry
Safe Responder Path Routing
IN CATASTROPHIC DISASTERS (LANDSLIDES, EARTHQUAKES), FIRST RESPONDERS FACE FOUR CRITICAL BARRIERS:
  COMMS BLACKOUT: Downed towers & power grids; cloud-AI drones rendered inoperable.
  ZERO VISIBILITY: Mud slush, smoke, and darkness blind standard visual cameras.
  HIGH MORTALITY: The Golden 72 Hours expire before manual foot sweeps reach victims.
  RESPONDER HAZARDS: Teams advance blindly into live wires, gas leaks, and shifting debris.
Project Phoenix: An autonomous, field-deployable multirotor scout engineered for offline disaster zones:
  100% ON-DEVICE AI: Executes real-time vision on Qualcomm silicon without internet.
  MULTI-SPECTRAL VISION: Fuses 4K RGB with LWIR Thermal (8-14μm) to spot living body heat (37°C).
  TAIT-BRYAN RAY-CASTING: Calculates victim Lat/Long GPS coordinates instantly from altitude.
  OFFLINE TACTICAL GCS: Streams priority triage queues and safe rescue routes to local operators.
Arduino UNO Q combining Qualcomm QRB2210 MPU + STM32U5 MCU in 40g.
INT8 quantized neural model running on NPU; preserves 90% power for flight.
Tait-Bryan rotation matrix projects bounding boxes to ground GPS pins.
17-byte bit-packed telemetry stream over 5+ km (Souli et al., Elsevier 2024).
Visual Odometry heading overrides magnetometer in steel rubble (Bouabdallah 2007).
Notes: 2

## Slide 3
TECHNICAL APPROACH
3
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Dual-Brain Architecture & Workflow
IMPLEMENTATION WORKFLOW
1
Sector Partition & Launch
Operator selects 2 km² search polygon on offline tablet; UAV launches in < 3 minutes.
2
Autonomous Grid Sweep
Executes Boustrophedon lawnmower coverage flight powered by STM32U5 / Zephyr RTOS at 250 Hz.
3
Multi-Spectral Perception
Dual 4K RGB + LWIR Thermal cameras co-register frames; edge YOLO extracts human heat contours.
4
Ray-Cast Geolocation
Tait-Bryan DCM matrix converts bounding box center + LiDAR altitude into real-world Lat/Long.
5
Binary LoRa Packet Burst
Souli et al. (2024) protocol packs survivor coordinates into 17-byte binary frame; broadcasts over 5+ km.
6
GCS Triage & Route Planning
Ground station ranks victims by accessibility, and can use the Dijkstra algorithm hazard-free ground efficient route.
SYSTEM ARCHITECTURE
Dual-Brain Hardware Split (Arduino UNO Q):
Real-Time MCU (STM32U585 / Zephyr RTOS):
  250 Hz (4ms) deterministic flight stabilization loop
  350 Hz PWM direct brushless motor control
  IMU (MPU6050) + Barometer (MS5611) + Downward LiDAR
Asynchronous non-blocking RPC bridge
Mission Computer (Qualcomm Dragonwing QRB2210 / Linux):
  INT8 YOLO Edge AI + Optical-to-Ground Ray-Caster
  Semtech SX1262 LoRa Telemetry Driver (868 MHz)
TECH STACK
Flight Stack
Zephyr RTOS, YMFC-32 Core, PX4 Autopilot
Edge AI & Vision
Qualcomm SNPE, ONNX Runtime INT8, OpenCV
Robotics Middleware
ROS2 Humble, MAVLink v2, micro-ROS
Long-Range RF Comms
Semtech SX1262 LoRa P2P (868 MHz)
Tactical GCS
React, Leaflet, Tailwind CSS, WebSockets
Security
HMAC-SHA256 Telemetry Packet Signatures
Notes: 3

## Slide 4
FEASIBILITY AND VIABILITY
4
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Feasibility, Challenges-to-Strategies & Market Viability
FEASIBILITY
TECHNICAL FEASIBILITY
  Bouabdallah Sizing Laws: 38% battery mass fraction, β ≥ 2.0 thrust-to-weight ratio.
  Total All-Up-Weight: 1.58 kg (Comfortably under DGCA 2.0 kg Micro Category).
  Sub-5W Compute: Qualcomm NPU preserves 90% power for rotor propulsion.
OPERATIONAL FEASIBILITY
  Setup Time: < 3 minutes from rugged backpack unboxing to flight.
  Quick-Swap Battery: Dual 4S LiPo tray for continuous sortie coverage.
FINANCIAL FEASIBILITY
  Prototype cost: 20,000₹
  Bill of Materials: ₹85,000 – ₹1,40,000 per operational unit.
VIABILITY
ECONOMIC VIABILITY
Enterprise Drone Disruption costs:
DJI Matrice 30T
₹10+ Lakhs
Phoenix
₹1.2 Lakh
Prototype cost: <40,000₹
  Fleet Scalability: NDRF battalions can deploy a swarm of 5 Phoenix UAVs for the price of 1 commercial drone.
NATIONAL DATA SOVEREIGNTY
  100% Air-Gapped: Zero telemetry leaked to foreign cloud servers; adheres to Indian Defense & Home Ministry cyber norms.
DEPLOYMENT ECOSYSTEM
  Seamless integration into state disaster management authorities (NDRF, SDRF, Indian Army disaster columns).
CHALLENGES → STRATEGIES
1
Comms Blackout in Canyons
→ Strategy: Raw LoRa P2P 868MHz packet burst (Souli et al., Elsevier 2024).
2
Smoke, Mud Slush & Darkness
→ Strategy: Dual-band 8-14μm LWIR Thermal fusion spots living 37°C body heat.
3
Rubble Steel Magnetometer Distortion
→ Strategy: Visual Inertial Odometry (VIO) overrides compass in magnetic fields.
4
Propeller Vibration Sensor Noise
→ Strategy: Zero-pitching-moment airfoils (NASA TM‑4741) + silicone mounts.
5
Actuator Saturation in Gusts
→ Strategy: Anti-windup integrator clamping (Bouabdallah Algorithm 2).
Notes: 4

## Slide 5
IMPACT AND BENEFITS
5
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Mission Impact & Multi-Stakeholder Benefits
TRAPPED VICTIMS
  Located in Golden 72h window
  Discovered through mud & debris
  Rapid medical triage prioritization
  Maximized chances of survival
NDRF / SDRF TEAMS
  Advance hazard mapping
  Avoid live cables & gas leaks
  Automated safe-route navigation
  Reduced physical rescuer fatigue
DISASTER AUTHORITIES
  Unified local tactical map
  Real-time survivor count & coords
  Zero dependency on cell towers
  Dynamic search sector logging
DISTRICT GOVERNANCE
  Efficient resource allocation
  Targeted airlift & medical drops
  Post-disaster audit trails
  Affordable procurement at scale
IMPACT PIPELINE
PHOENIX DOES
IMPACT
MEASURE
1 DEPLOY
Backpack to flight with no infrastructure
Search starts within minutes of arrival
< 3 min
unboxing to flight
2 SEARCH
Flies an autonomous sweep with RGB + thermal vision
Search continues at night and in smoke or fog
2 km²
search sector
3 LOCATE
Pins each detected survivor with GPS coordinates
Rescuers go straight to survivors, not digging blind
0 cell towers
needed to report locations
4 RESPOND
Ranks survivors and plots a hazard-free route
Crews avoid cave-ins, gas leaks and live cables
Ranked queue
+ safe rescue route
5 OUTCOME
Delivers all this at a fraction of enterprise-drone cost
More survivors reached in the Golden 72 hours
₹1.2 Lakh
vs ₹12-14 Lakhs
Notes: 5

## Slide 6
RESEARCH AND REFERENCES
6
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Academic Research Foundations & Prototype Verification
RESEARCH & REFERENCES
PROTOTYPE PROOF
01
Dr. Samir Bouabdallah (EPFL Thesis 3727, 2007)
  'Design and Control of Quadrotors with Application to Autonomous Flying'
  Sourced 12-state rigid-body dynamics, 90/10 electrical power rule, and anti-windup integrator.
02
Souli, Karatzia, Kolios, Ellinas (Elsevier, 2024)
  'Mission-critical UAV swarm coordination using integrated ROS-LoRa architecture' (Computer Communications, Vol. 225)
  Sourced 17-byte binary bit-packing & P2P LoRa telemetry.
03
NASA Technical Memorandum 4741 (NASA Langley, 1996)
  'Computer Program To Obtain Ordinates for NACA Airfoils'
  Sourced zero-pitching-moment (Cm=0) reflexed airfoil theory to eliminate blade flutter and IMU noise.
04
JRFCQAI Dual-Brain Platform (Ravi Butani, 2024)
  'Dual-Brain Physical AI Flight Controller on Arduino UNO Q'
  Established Zephyr RTOS + Debian Linux on Qualcomm QRB2210.
OPEN-SOURCE REPOSITORY & VERIFICATION ASSETS
Presentation Video:
Web Demo:
Github Repo:
phoenix-sar-uav.vercel.app
github.com/jvstin47/Phoenix
Documented Subsystems:
1. docs/bouabdallah_quadrotor_research_findings.md
2. docs/ros_lora_mission_critical_uav_swarm_research.md
3. docs/aerodynamic_airfoil_considerations.md
4. presentation/sih_presentation_outline.md
Prototype Architecture Deliverables:
Live Web GCS Tactical Dashboard (React + Leaflet)
Multi-Spectral Dual Stream (RGB + LWIR Thermal HUD)
LoRa 17-Byte Binary Bit-Packing Serialization Module
Ray-Casting Geolocation Python Engine
Notes: 6