## Slide 1
SMART INDIA HACKATHON 2026
HARDWARE EDITION | MINISTRY OF EDUCATION & QUALCOMM INC.
PROJECT PHOENIX X
SAR UAV
Dual-Brain Edge-AI Scout for Zero-Infrastructure Disaster Reconnaissance
PROBLEM STATEMENT ID
SIH26177
THEME
Robotics and Drones
PROBLEM STATEMENT TITLE
A deployable AI-powered autonomous drone that aids search-and-rescue operations by detecting people and hazards, thereby improving responder safety and reducing victim discovery time.
SPONSORING ORGANIZATION
CATEGORY
Qualcomm Inc.
Hardware
TEAM NAME
TEAM ID
Phoenix X
141943
WEB DEMO
VIDEO
Qualcomm Dragonwing QRB2210
STM32U5 Zephyr RTOS Flight
Dual RGB + Thermal Fusion
3-5 km LoRa Telemetry
IEEE Anti-Drift VIO Navigation

## Slide 2
Disaster Reconnaissance & Emergency Survivor Triage
2
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
PROBLEM STATEMENT
PROPOSED SOLUTION
INNOVATION / UNIQUENESS
Dual-Brain Architecture
5W Edge YOLO
Ray-Cast Geolocation
ROS-LoRa P2P Bridge
Anti-Compass Drift VIO
TRADITIONAL DISASTER SEARCH
(Current Approach)
Manual Foot Sweeps
Blind Rubble Digging
Stalled at Sunset (Darkness)
High Responder Casualty Risk
Critical Hours Lost
PHOENIX AUTONOMOUS SAR
(Our Approach)
Autonomous Aerial Sweep
24/7 Thermal Night Vision
Instant Survivor GPS Raycasting
Zero-Drop LoRa Telemetry
Safe Responder Path Routing
IN CATASTROPHIC DISASTERS (LANDSLIDES, EARTHQUAKES), FIRST RESPONDERS FACE FOUR CRITICAL BARRIERS:
COMMS BLACKOUT: Downed cellular towers & power grids; cloud-dependent drones rendered completely inoperable.
ZERO VISIBILITY: Mud slush, dense smoke, and darkness blind standard visual electro-optical cameras.
ENTRAPMENT ACCESS: Survivability sharply declines with delayed response; manual foot searches cannot cover wide rubble sectors in time.
RESPONDER HAZARDS: Ground teams advance blindly toward fallen electrical wires, gas leaks, and secondary landslides.
Project Phoenix: An autonomous, field-deployable multirotor scout engineered for offline disaster zones:
100% ONBOARD EDGE COMPUTE: Heterogeneous AI (CPU/GPU/DSP) executes all vision & geolocation on-device; zero cloud/cellular dependency.
MULTI-SPECTRAL FUSION: Combines 4K RGB with LWIR Thermal (8-14μm) to spot surface heat anomalies & exposed casualties through smoke/darkness.
TAIT-BRYAN RAY-CASTING: Calculates victim ground GPS coordinates on the fly from altitude without battery-wasting hovering.
LIGHTWEIGHT OFFLINE GCS: Low-power field tablets receive 17-byte pins; charts priority triage queues & safe walking corridors [1].
Arduino UNO Q (4GB LPDDR4 / 32GB eMMC): Qualcomm Dragonwing QRB2210 MPU + STM32U585 MCU on a unified 40g board.
Heterogeneous On-Device AI: CPU/Adreno GPU/Hexagon DSP executes INT8 YOLO vision; draws ~3.5W under peak inference.
Tait-Bryan Ray-Casting: Converts camera ray & ToF laser altitude to ground GPS pins on the fly without hovering.
Resilient LoRa P2P Telemetry: 17-byte bit-packed telemetry stream over 3–5+ km in blackout zones (Souli et al. [3], 2024).
Anti-Compass Drift VIO: Visual-Inertial Odometry overrides magnetometer in collapsed steel rubble (IEEE standard navigation).
Notes: 2

## Slide 3
TECHNICAL APPROACH
3
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Dual-Brain Architecture & Workflow
IMPLEMENTATION WORKFLOW
1
Sector Partition & Launch
Operator selects 2 km² search polygon on offline tablet; UAV launches in < 3 minutes.
2
Autonomous Grid Sweep
Boustrophedon decomposition with 60% sidelap & 70% overlap; ToF altimeter maintains constant GSD over sloped terrain.
3
Multi-Spectral Perception
Dual 4K RGB + LWIR Thermal fusion; edge YOLO detects survivor heat anomalies (37°C) & flags surface obstacles for flight avoidance.
4
Ray-Cast Geolocation
Transforms 2D bbox offset via 3D Tait-Bryan DCM matrix & ToF altitude (ΔP = H_AGL · R·v) to pin GPS on the fly.
5
Binary LoRa Packet Burst
Onboard Triage & LoRa Burst: UAV computes victim priority on-chip & packs coordinates into 17-byte binary frame [3]; broadcasts over 868 MHz.
6
GCS Triage & Route Planning
Lightweight Offline GCS: Low-power tablet receives 17-byte pins; charts hazard-aware Dijkstra safe walking corridor [1] avoiding live electrical lines.
SYSTEM ARCHITECTURE
Dual-Brain Hardware Split (Arduino UNO Q):
Real-Time MCU (STM32U585 / Zephyr RTOS):
  250 Hz (4ms) deterministic flight stabilization loop
  350 Hz PWM direct brushless motor control
  IMU (MPU6050) + Barometer (MS5611) + Downward LiDAR
Asynchronous non-blocking RPC bridge
Mission Computer (Qualcomm Dragonwing QRB2210 / Linux):
  Qualcomm Dragonwing QRB2210 (Debian Linux — 4GB RAM, 32GB eMMC)
Heterogeneous On-Device AI (CPU/GPU/DSP) // Ray-Caster // SX1262 LoRa Driver [3]
TECH STACK
Flight Stack
Zephyr RTOS, YMFC-32 Core, PX4 Autopilot
Edge AI & Vision
YOLOv8n INT8 (Detection & Avoidance), SNPE SDK, ONNX, OpenCV
Robotics Middleware
ROS2 Humble, MAVLink v2, micro-ROS
Long-Range RF Comms
Semtech SX1262 LoRa P2P (868 MHz)
Tactical GCS
React, Leaflet, Tailwind CSS, WebSockets
Security
HMAC-SHA256 Telemetry Packet Signatures
Notes: 3

## Slide 4
FEASIBILITY AND VIABILITY
4
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Feasibility, Challenges-to-Strategies & Market Viability
FEASIBILITY
TECHNICAL FEASIBILITY
  Propulsion Sizing: 38% battery mass fraction, β ≥ 2.0 thrust-to-weight ratio.
All-Up-Weight: 1.58 kg mass budget (Comfortably under DGCA 2.0 kg Micro Category).
Sub-6W Electronics Payload: Onboard compute draws ~5.5W under peak AI (>96% power for flight).
OPERATIONAL FEASIBILITY
  Setup Time: < 3 minutes from rugged backpack unboxing to flight.
Quick-Swap Battery: Dual 4S LiPo tray for continuous sortie coverage.
Zero Ground Compute Burden: 100% onboard processing enables deployment via low-power tablets or handheld LoRa pagers.
FINANCIAL FEASIBILITY
  Prototype Build: ₹37,400 (Calibrated Prototype — Arduino UNO Q 4GB/32GB).
Production BOM: ₹85,000 – ₹1,20,000 per unit (10x cheaper than commercial enterprise drones).
VIABILITY
ECONOMIC VIABILITY
Enterprise Drone Disruption costs:
DJI Matrice 30T
₹10+ Lakhs
Phoenix
₹1.2 Lakh
Prototype cost: <40,000₹
  Fleet Scalability: NDRF battalions can deploy a swarm of 5 Phoenix UAVs for the price of 1 commercial drone.
NATIONAL DATA SOVEREIGNTY
  100% Air-Gapped: Zero telemetry leaked to foreign cloud servers; adheres to Indian Defense & Home Ministry cyber norms.
DEPLOYMENT ECOSYSTEM
  Seamless integration into state disaster management authorities (NDRF, SDRF, Indian Army disaster columns).
CHALLENGES → STRATEGIES
1
Comms Blackout in Canyons
→ Strategy: 868MHz LoRa packet bridge in NLoS canyons [2] (Pérez-Díaz-de-Cerio, IEEE Access 2026, DOI: 10.1109/ACCESS.2026.3731317).
2
Smoke, Mud Slush & Darkness
→ Strategy: 8-14μm LWIR thermal anomaly detection in dense smoke & fog [1] (Siotia et al., IEEE Access 2026, DOI: 10.1109/ACCESS.2026.3730315).
3
Rubble Steel Magnetometer Distortion
→ Strategy: Visual-Inertial Odometry overrides magnetometer in collapsed steel rubble (IEEE standard navigation).
4
Propeller Vibration Sensor Noise
→ Strategy: Notch-filtered EKF & silicone harmonic vibration dampening (IEEE Control Systems & Robotics).
5
Actuator Saturation in Gusts
→ Strategy: Anti-windup integrator clamping on 250Hz deterministic PID loop (IEEE Industrial Electronics).
Notes: 4

## Slide 5
IMPACT AND BENEFITS
5
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Mission Impact & Multi-Stakeholder Benefits
TRAPPED VICTIMS
  Located in Golden 72h window
  Discovered through mud & debris
  Rapid medical triage prioritization
  Maximized chances of survival
NDRF / SDRF TEAMS
  Advance hazard mapping
  Avoid live cables & gas leaks
  Automated safe-route navigation
  Reduced physical rescuer fatigue
DISASTER AUTHORITIES
  Unified local tactical map
  Real-time survivor count & coords
  Zero dependency on cell towers
  Dynamic search sector logging
DISTRICT GOVERNANCE
  Efficient resource allocation
  Targeted airlift & medical drops
  Post-disaster audit trails
  Affordable procurement at scale
IMPACT PIPELINE
PHOENIX DOES
IMPACT
MEASURE
1 DEPLOY
Backpack to flight with no infrastructure
Search starts within minutes of arrival
< 3 min
unboxing to flight
2 SEARCH
Flies an autonomous sweep with RGB + thermal vision
Search continues at night and in smoke or fog
2 km²
search sector
3 LOCATE
Pins each detected survivor with GPS coordinates
Rescuers go straight to survivors, not digging blind
0 cell towers
needed to report locations
4 RESPOND
Ranks survivors and plots a hazard-free route
Crews avoid cave-ins, gas leaks and live cables
Ranked queue
+ safe rescue route
5 OUTCOME
Delivers all this at a fraction of enterprise-drone cost
More survivors reached in the Golden 72 hours
₹1.2 Lakh
vs ₹12-14 Lakhs
Notes: 5

## Slide 6
RESEARCH AND REFERENCES
6
PROJECT PHOENIX: Autonomous Multi-Spectral Edge-AI UAV | SIH26177 (Qualcomm Inc.)
Academic Research Foundations & Prototype Verification
RESEARCH & REFERENCES
PROTOTYPE PROOF
01
IIT Jodhpur & Manipal (IEEE Access, Sept 2026) [1]
  • 'SwarmSAR-FW: Drone-Based Swarm Search and Rescue in Fire and Water Disasters'
• Sourced & validated Hazard-Aware Safe Access Ingress Routing for ground crews & 98.7% triage.
DOI: 10.1109/ACCESS.2026.3730315 (Direct IEEE Document Link)
02
UPC Spain & Souli et al. (IEEE Access 2026 / Elsevier 2024) [2, 3]
  • 'Long-Range BLE Detection via Drone LoRa Relays' [2] & 'Mission-Critical ROS-LoRa Architecture' [3]
• Sourced 868 MHz LoRa off-grid data bridge & 17-byte binary telemetry in cellular blackout zones.
DOIs: 10.1109/ACCESS.2026.3731317 [2] | 10.1016/j.comcom.2024.04.015 [3]
03
TalTech Estonia & SARDO (IEEE Access 2023 / IEEE TMC 2022) [4, 5]
  • 'Applying RIS-Based Comm for Collaborative Computing' [4] & 'SARDO RF Victim Localization' [5]
• Validated decentralized swarm edge-computing without cloud servers (-32% energy); 1/8th weight vs SDR.
DOIs: 10.1109/ACCESS.2023.3293737 [4] | 10.1109/TMC.2022.3168331 [5]
04
BITS Pilani & van Tilburg (Elsevier 2020 / Wilderness Med 2017) [6, 7]
  • 'Drone Surveillance & Human Action Detection' [6] & 'First Report of Using Drones for SAR' [7]
• Validates 2000+ aerial human detection dataset for INT8 YOLO and operational field unboxing protocols.
DOIs: 10.1016/j.comcom.2020.03.042 [6] | 10.1016/j.wem.2017.06.004 [7]
OPEN-SOURCE REPOSITORY & VERIFICATION ASSETS
Video link: SIH Grand Finale Submission Portal
Presentation Video:
Web Demo:
Github Repo:
phoenix-sar-uav.vercel.app
github.com/jvstin47/Phoenix-SIH26177-SAR-UAV
Documented Subsystems:
1. docs/research_papers_synthesis_2026.md
2. docs/prototype_bom_and_financial_viability.md
3. docs/ros_lora_mission_critical_uav_swarm_research.md
4. docs/bouabdallah_quadrotor_research_findings.md
Prototype Architecture Deliverables:
Live Web GCS Tactical Dashboard (React + Leaflet)
Multi-Spectral Dual Stream (RGB + LWIR Thermal HUD)
LoRa 17-Byte Binary Bit-Packing Serialization Module
Ray-Casting Geolocation Python Engine
Notes: 6