## Slide 1
SMART INDIA HACKATHON 2026 | HARDWARE EDITION
PROJECT PHOENIX: AUTONOMOUS SEARCH & RESCUE UAV
Deployable Multi-Spectral Edge-AI Drone for Rapid Victim Localization & Hazard Reconnaissance in Communication-Denied Disasters
• Problem Statement ID: SIH26177 | Theme: Robotics and Drones | Category: Hardware
• Sponsoring Organization: Qualcomm Inc.
• Team Name: Team Phoenix | Domain: CSE + AI & Data Science + Cyber Security (2nd Year Undergraduates)

## Slide 2
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT ID: SIH26177
The Critical Need: Disaster Reconnaissance in the 'Golden 72 Hours'
1. Communication Blackout
• Severe Disconnection: Earthquakes, landslides (e.g. Wayanad 2024), and floods instantly sever 4G/5G mobile towers and electrical grids. • Cloud-AI Fails: Standard consumer drones rely on cellular telemetry or cloud processing, rendering them completely blind and inoperable in the disaster epicentre. • First Responder Disconnect: Ground crews operate with zero real-time situational awareness.
2. Environmental Occlusion
• Slush, Smoke & Darkness: Debris, thick rain clouds, and smoke plumes camouflage survivors from ordinary visual (RGB) aerial cameras. • Night Stoppage: Search operations are traditionally halted at sunset when optical visibility drops to zero, wasting crucial survival hours. • The Rubble Trap: Survivors trapped under light sheet debris remain invisible to human spotters.
3. Responder Hazard & Latency
• High Mortality Curve: Victim survival drops precipitously after the first 72 hours; manual foot sweeps take days to cover a 2 km² disaster area. • Secondary Disasters: Responders walk blindly into secondary hazards: active gas leaks, submerged live powerlines, and unstable structural slopes. • Solution Mandate: Need rapid autonomous aerial triage before deploying ground rescuers.

## Slide 3
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT ID: SIH26177
Proposed Solution: Project Phoenix Autonomous SAR UAV
Core Solution Overview
Project Phoenix is a deployable autonomous multirotor UAV designed to act as an offline-first aerial reconnaissance scout for NDRF and SDRF teams: • 100% Onboard Edge Intelligence: Operates without internet, cellular connectivity, or external cloud infrastructure. • Multi-Spectral Vision Core: Co-registered RGB + Long-Wave Infrared (LWIR) thermal sensors detect living human body heat signatures (36°C-38°C) through smoke, mud, and total night darkness. • Tait-Bryan Ray-Casting Geolocation: Instantly converts 2D bounding boxes into real-world GPS coordinates without hovering overhead. • Offline Responder GCS: Displays live victim pins, hazard heatmaps, and shortest hazard-free ground rescue routes on a local tablet.
Key Technical Innovations
• Dual-Brain Architecture on Single Board: Powered by the Arduino UNO Q integrating the Qualcomm Dragonwing™ QRB2210 Linux MPU with an STM32U585 Real-Time MCU (replaces both flight controller & companion computer in 40g). • Sub-5W Edge Deep Learning: INT8-quantized YOLO model running on the Qualcomm NPU; complies with Bouabdallah's 90/10 power rule (actuators consume 90%, compute draws < 10%). • Dual-Tier Resilient Telemetry: High-bandwidth Wi-Fi mesh for nearby video + ultra-reliable LoRa (868 MHz) emergency beacon transmitting coordinates over 5+ km. • Anti-Compass Drift Heading: Visual-Inertial Odometry overrides magnetometers in steel rubble.

## Slide 4
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT ID: SIH26177
Technical Architecture: The Dual-Brain Edge Pipeline
Step 1: Sensing
Dual-Band Sensor Suite
• Sony 4K RGB Camera for terrain context & visual markers. • Infiray / FLIR LWIR Thermal Sensor (8-14μm) for human heat anomalies. • Downward LiDAR/Sonar for precise ground distance and altitude. • Anti-vibration silicone dampening platform.
Step 2: Real-Time MCU
STM32U585 Core @ 250Hz
• Runs Zephyr RTOS with hard-deterministic 4ms PID flight loops. • Inherits Joop Broking YMFC-32 flight stabilization heritage. • 350Hz patched PWM for direct brushless ESC response. • Asynchronous RPC bridge prevents Linux tasks from blocking flight.
Step 3: Edge AI MPU
Qualcomm QRB2210 Core
• Debian Linux host executing INT8 quantized YOLO-nano. • Multi-spectral late fusion: blends RGB confidence with thermal heat. • Tait-Bryan Ray-Casting: Calculates victim Lat/Long using drone altitude and gimbal attitude. • Sub-5W power draw.
Step 4: Tactical GCS
Offline Ground Station
• Dual comms: Local Wi-Fi video stream + LoRa 868MHz packet telemetry. • Offline vector disaster mapping (Leaflet / Mapbox tiles). • Automated Triage Queue (coordinates, confidence, heat). • Dijkstra safe-path routing for ground search crews.

## Slide 5
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT ID: SIH26177
Engineering Feasibility & Commercial Viability
Mathematical Sizing (Bouabdallah Sizing Laws)
• Thrust-to-Weight Ratio: β ≥ 2.0 (50% thrust margin for turbulence, heavy wind, and evasive climb in disaster zones). • 38% Battery Mass Fraction: Sized via Bouabdallah's Cost Factor (C) and Autonomy (Au) optimization; prevents payload-diminishing returns. • Weight Budget (Under DGCA 2kg Micro Limit): - Airframe & 4x BLDC Motors + Props: 720g - Battery (4S 5200mAh LiPo): 560g - Dual-Brain Avionics (UNO Q + Sensors): 120g - Dual-Camera Gimbal Payload: 180g - Total All-Up-Weight (AUW): 1.58 kg (< 2.0 kg Micro Category) • 30-Minute Search Window: Covers 1.5 km² grid per battery sortie.
Market & Cost Viability Comparison
Current Commercial Standard (e.g. DJI Matrice 30T): • Unit Cost: ₹9,00,000 to ₹14,00,000 (Exorbitant for regional SDRF) • Closed Ecosystem: Locked firmware, foreign server telemetry risk. • No Custom Edge AI: Cannot deploy custom disaster hazard models. Project Phoenix SAR Platform: • Estimated Unit Cost: ₹85,000 to ₹1,40,000 (1/8th of the cost!) • Open-Source Dual-Brain Stack: 100% Indian data sovereignty. • Edge Programmability: Deploy updated neural models over USB. • Rapid Deployment: < 3 minutes from unboxing to takeoff. • Swarm Scalable: 1 disaster battalion can deploy 5 Phoenix units for the price of 1 proprietary enterprise drone.

## Slide 6
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT ID: SIH26177
Research Foundations & Team Phoenix Competency
Research Foundations & Prior Art
1. Dr. Samir Bouabdallah (EPFL Thesis No. 3727, 2007): • 'Design and Control of Quadrotors with Application to Autonomous Flying' • Grounded our 12-state rigid body dynamics, spectral loop separation, and the 90/10 electrical power sizing law. 2. NASA Technical Memorandum 4741 (NASA Langley, 1996): • Informed selection of zero-pitching-moment (Cm=0) reflexed airfoils to eliminate blade flutter and IMU vibration. 3. JRFCQAI Open-Source Dual-Brain Architecture (Ravi Butani, 2024): • Established the viability of Zephyr RTOS (STM32U5) + Debian Linux (Qualcomm QRB2210) on the Arduino UNO Q for UAV flight.
Team Phoenix Synergy & Execution Plan
• AI & Data Science (AD): - Multi-spectral RGB + Thermal dataset curation & augmentation. - INT8 model quantization for the Qualcomm Dragonwing NPU. • Computer Science & Engineering (CSE): - Tait-Bryan Ray-Casting coordinate projection engine. - Offline Web Ground Station (React + Leaflet + WebSocket bus). • Cyber Security (CY): - Telemetry packet authentication & anti-spoofing. - LoRa emergency telemetry fallback protocol & store-and-forward sync. GitHub Repository: github.com/jvstin47/Phoenix-SIH26177-SAR-UAV